## Slide 1
SCOOT 8 AI
TRAFFIC
MANAGEMENT
SYSTEMS
Why cities need a live feedback loop
Sense demand → coordinate signals → measure outcomes
1
SENSE
2
UNDERSTAND
3
DECIDE
4
ACT
5
LEARN
Jitesh Anand • Roll 124109004 • IIoT A-(1)
Traffic is dynamic.
Signals must be dynamic too.
Visual: internet-sourced traffic image • Source: Adaptive Traffic Signal Timer repository

## Slide 2
THE NEED
Bengaluru: the cost of unmanaged demand
02
36:09
per 10 km
average travel time
13.9 km/h
rush-hour speed
citywide average
168 h
lost each year
per rush-hour driver
Demand changes by minute; fixed plans change by schedule.
Weather • events • crashes • school peaks • bus bunching
74.4% congestion
2025
Traffic figures: TomTom Traffic Index, Bengaluru 2025 • City images: Wikispeedia/Wikipedia archive
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 3
WHY ADAPTIVE CONTROL
From fixed-time to predictive control
03
⏱
FIXED
Repeat a plan
↻
ADAPTIVE
Respond to now
+30
PREDICTIVE
Prepare for next
same sequence
live demand
forecast horizon
reactive
proactive
Conceptual progression; predictive horizon based on TRL’s SCOOT 8 AI announcement
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 4
DEVELOPMENT
SCOOT: an evolving control philosophy
04
Split • Cycle • Offset
Optimisation Technique
1977
Research birth
1980s–2000s
Global rollout
2024
SCOOT 8
2025
SCOOT 8 AI
350+
towns & cities
SCOOT family footprint
Nearly 50 years of field evolution
Small, frequent timing changes across a coordinated network
Sources: TRL Software SCOOT 8 (2024) and SCOOT 8 AI launch (2025) • Signal image: Adaptive Traffic Signal Timer repo
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 5
DEVELOPMENT
SCOOT 8: the development leap
05
From traffic control to traffic intelligence
AUTO-VALIDATE
Initial validation + continuous revalidation
ANALYTICS
Second-by-second performance measures
MULTIMODAL
Pedestrian demand in split + cycle decisions
ANOMALIES
R&D with Alan Turing Institute candidates
47 YEARS
of operating knowledge
inside the next platform
Source: TRL Software presentation, “SCOOT 8 – 47 Years Later” (2024) • Visual: Apache-licensed traffic project repo
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 6
TRL-REPORTED
SCOOT 8 AI: headline achievements
06
30 min
traffic forecast
look-ahead horizon
up to 15%
journey time
vs current-generation systems
up to 40%
faster detection
incidents + anomalies
≤12 mo
typical ROI
vendor estimate
AI adds foresight
Forecast demand • flag anomalies • recommend action
Hardware-agnostic
Real-time dashboards
3rd-party data
Treat these as claims to validate under local pilot conditions.
Source: TRL Software, SCOOT 8 AI launch, 23 Sep 2025 • Detection visual: Adaptive Traffic Signal Timer repo
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 7
TECHNOLOGY
SCOOT 8 AI: broad system architecture
07
INPUTS
INTELLIGENCE
ACTIONS
Loops • cameras • radar
Connected data
Transit + pedestrian demand
AI
Digital flow model
Demand forecast
Network optimisers
Anomaly detection
Signal plans • priority
Alerts + dashboards
Operator decisions
External traveller info
Hardware-agnostic software layer over compatible field controllers
Architecture synthesized from TRL SCOOT 8/8 AI material and FHWA SCOOT descriptions • Internet visuals credited on slide 20
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 8
TECHNOLOGY
From detector pulse to green time
08
1
DETECT
flow • speed
2
CLEAN
health • fuse
3
ESTIMATE
queues • platoons
4
FORECAST
0 → 30 min
5
OPTIMISE
cycle • split • offset
6
COMMAND
controller
SECOND-BY-SECOND
measure + update state
EACH CONTROL STEP
test small timing changes
+30 MINUTES
prepare for demand
↺
measure outcome
Sources: TRL SCOOT 8/8 AI; FHWA Traffic Detector Handbook • Detection visual: Adaptive Traffic Signal Timer repo
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 9
CLASSIC SCOOT
The three controls inside SCOOT
09
CYCLE
SPLIT
OFFSET
90 s
Total time for one
signal sequence
Longer when network demand rises
N–S
E–W
How the cycle is
shared as green
More demand → more useful green
A
B
Start-time shift between
neighbouring signals
Align greens with arriving platoons
Source: FHWA Traffic Detector Handbook and FHWA SCOOT overview
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 10
AI LAYER
Predictive control: act before the queue forms
10
NOW
+30 min
Predicted demand
Pre-position green
before spillback
ANOMALY
REACTIVE
Respond after queues are measured
PREDICTIVE
Respond to likely future demand
Source: TRL Software SCOOT 8 AI announcement (forecast horizon and anomaly detection claims)
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 11
CONTROL LOGIC
A closed loop that learns every cycle
11
SCOOT
8 AI
OBSERVE
ESTIMATE
FORECAST
TEST
ACT
MEASURE
Objective
minimise delay + stops
within safety constraints
Small changes • frequent checks • operator visibility
Conceptual loop synthesized from FHWA SCOOT descriptions and TRL SCOOT 8 material
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 12
MULTIMODAL CONTROL
One network, many road users
12
BUS
reliability
WALK
safe crossing
CYCLE
progression
EMERGENCY
priority path
PRIORITY ≠ ALWAYS GREEN
Minimum greens • pedestrian clearance • queue limits • network balance
Policy constraints stay above optimisation.
Source: TRL SCOOT 8 multimodal features • Internet visuals: Ultralytics, PyTorch Hub, Wikispeedia, Apache traffic project
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 13
COMPETITOR COMPARISON
SCOOT 8 AI vs SCATS vs Surtrac
13
CRITERION
SCOOT 8 AI
SCATS
SURTRAC
Control style
Network model + predictive UTC
Real-time adaptive network
Distributed local scheduling
Look-ahead
Up to 30 min
Primarily live adaptive
Short-horizon neighbour plans
Architecture
Central platform + field controllers
Hierarchical / scalable
Intersection agents
Best fit
Coordinated corridors + city networks
Large mature signal networks
Local grids / edge autonomy
Published reach
350+ towns & cities*
60,000+ intersections
50 Pittsburgh sites†
* SCOOT family footprint • † CMU figure as of 2019
No universal winner
Sources: TRL Software; SCATS official site; Carnegie Mellon University Surtrac profile • Different product claims and dates
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 14
EVIDENCE, WITH CONTEXT
What the published numbers actually say
14
15%
journey time
SCOOT 8 AI • TRL vendor claim
12%
delay
London SCOOT • GLA average
25%
travel time
Surtrac • CMU Pittsburgh report
33%
travel time
Bengaluru B-ATCS • reported peaks
These are not head-to-head benchmarks.
Baselines, networks, study periods and reporting methods differ.
Use them to set the order of magnitude—not to promise a Bengaluru result.
Pilot → measure → compare with a pre-agreed baseline
Sources: TRL (2025); Greater London Authority; CMU (2019); Indian Express report on Bengaluru B-ATCS (2024)
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 15
DESIGN ASSESSMENT
Which system fits an Indian corridor?
15
1
5
Network coordination
Retrofit potential
Distributed resilience
Published scale
SCOOT 8 AI
SCATS
SURTRAC
BEST PILOT HYPOTHESIS
SCOOT 8 AI: predictive corridor coordination + controller retrofit—subject to interface audit and local validation.
Scores are an author assessment for the proposed Bengaluru corridor.
Assessment based on published architecture, footprint and Bengaluru integration needs; it is not a vendor benchmark
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 16
PROPOSED IMPLEMENTATION
Bengaluru pilot concept
16
CONCEPT — NOT AN ANNOUNCED DEPLOYMENT
PURPLE CORRIDOR
SURFACE NETWORK
MG Road → Trinity → Halasuru → Indiranagar
8–12
junctions
after field audit
26
weeks
baseline to review
1
corridor
prove then scale
Integrate with existing Bengaluru adaptive-control assets where interfaces permit.
City visuals: Wikispeedia/Wikipedia archive • Existing context: Bengaluru Traffic Police ATCS and reported B-ATCS rollout
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 17
BENGALURU CORRIDOR
Pilot architectural map
17
FIELD CORRIDOR
MG ROAD
S1
TRINITY
S2
HALASURU
S3
INDIRANAGAR
S4
J
J
J
J
TRAFFIC
MANAGEMENT
CENTRE
SCOOT 8 AI
secure IP / fibre / 4G
FIELD
Cameras • loops • radar
signals • UPS
GATEWAY
Existing B-ATCS interface
protocol + health checks
PLATFORM
Model • forecast • optimise
logs + safe fallback
USERS
TMC • traffic police • BMTC
dashboards + traveller data
Conceptual architecture — controller protocol, junction count and exact route require field survey.
Architecture authored for this presentation using TRL/FHWA system descriptions and Bengaluru ATCS context
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 18
PILOT DELIVERY
Implementation roadmap: 26 weeks
18
0
BASELINE
4 weeks
Audit controllers
Collect travel-time + stop data
1
SHADOW MODEL
6 weeks
Build network model
Run offline; calibrate
2
LIVE PILOT
12 weeks
Controlled activation
Daily health review
3
EVALUATE
4 weeks
Before/after analysis
Scale or revise
PROPOSED SUCCESS THRESHOLDS
–10%
median corridor time
–10%
stops
–12%
bus p90 time
≥95%
detector uptime
SAFETY GATE: validated minimum greens + red clearance + automatic fallback to approved timings
Durations and KPI thresholds are proposed for planning; finalize after the baseline audit
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 19
INDIAN DEPLOYMENT
Advantages, challenges—and safeguards
19
ADVANTAGES
CHALLENGES + RESPONSE
Fewer stops
network coordination
More reliable buses
conditional priority
Earlier incident response
predictive anomalies
Transparent performance
live KPIs + audit trail
Mixed, weak lane discipline
train + calibrate on local classes
Monsoon + occlusion
sensor fusion + health monitoring
Legacy interfaces
controller audit + tested gateway
Power, data, skills
UPS + fallback + role-based ops
Optimisation is useful only when detection, safety and operations are dependable.
Challenge analysis authored for Bengaluru conditions • Background visual: DI-drive open-source simulator
Jitesh Anand • 124109004 • IIoT A-(1)

## Slide 20
START WITH ONE CORRIDOR.
PROVE IT. SCALE BY EVIDENCE.
BASELINE
before activation
FAIL-SAFE
approved timings
OPEN KPIs
public outcomes
The recommendation
A measured Bengaluru corridor pilot that treats AI as a controlled transport intervention.
KEY SOURCES
1. TRL Software — SCOOT 8 AI (2025)
2. TRL — SCOOT 8 presentation (2024)
3. FHWA — Traffic Detector Handbook
4. SCATS — official system overview
5. Carnegie Mellon — Surtrac (2019)
6. TomTom — Bengaluru Traffic Index 2025
7. Bengaluru Traffic Police — ATCS
8. Indian Express — B-ATCS results (2024)
9. Images: Wikispeedia/Wikipedia archive
10. Images: Adaptive Traffic Signal Timer
11. Images: Ultralytics • PyTorch • DI-drive
Full links + speaking script are in the companion notes file.
Jitesh Anand • 124109004 • IIoT A-(1)